## Slide 1: Study of the Scintillation Induced by Interactions for Neutrino Measurements
A. Ben Porat
Tel Aviv University – Student Seminar July 2025
avivbenporat@mail.tau.ac.il
1

## Slide 2: Background Neutrino Oscillation
Neutrino oscillation is a quantum phenomenon where neutrinos change flavor as they propagate.
Key Concepts:
Neutrinos interact only via weak force
Flavor states:
Mass states:
PMNS Matrix: Relates flavor ↔ mass eigenstates
Implications:
non-zero neutrino mass
Probes physics beyond the Standard Model
Probes CP violation in the lepton sector
P. Fernandez PhD Thesis

## Slide 3: Neutrino detection challenge
Neutrinos have a very low cross section for interaction since they only interact weakly
They are neutral and thus invisible in our detectors
Need to study them via their interaction products

## Slide 4: Motivation
Neutrons are invisible in neutrino detectors but crucial for reconstructing neutrino energy.
Neutrons are involved in ~40% of interactions → large bias risk.
Assist neutrino oscillation experiments by improving neutron detection in LArTPCs via scintillation light.

## Slide 5: Background Liquid Argon Time Projection Chambers (LArTPCs)
Working mechanism:
• Incoming charged particle ionizes the LAr
• Ionization electrons drift to collection wires which readout the charge, providing x,y coordinates of the ionization electrons
• Scintillation light provides t₀ of the interaction, which enables to determine the drift distance and the z (drift direction) coordinates
PMT
Scintillation Light
Notes: LArTPCs are high-resolution detectors used to map 3D tracks of particles

## Slide 6
Background Scintillation in Liquid Argon
2009 J. Phys.: Conf. Ser. 160 012032
Notes: The passage of ionizing particles in LAr can produce excited, or ionized, , argon dimers.
can recombine with a thermalized electron to form , which in turn decay non-radiatively to either a singlet or triplet state.
The de-excitation of these states leads to the emission of scintillation light of approximately the same wavelength – 128nm, while their lifetimes are very different: ~ 7ns for the singlet and ~1.5 for the triplet state
The presence of an electric field can drift thermalized electrons, preventing them from recombining and reducing the scintillation yield
The passage of ionizing particles in LAr can produce excited 𝐴𝑟_2^∗, or ionized, 𝐴𝑟_2^+ , argon dimers.
𝐴𝑟_2^+ can recombine with a thermalized electron to form 𝐴𝑟_2^∗, which in turn decay non-radiatively to either a singlet or triplet state.
The de-excitation of these states leads to the emission of scintillation light of approximately the same wavelength – 128nm, while their lifetimes are very different: ~ 7ns for the singlet and ~1.5𝜇𝑠 for the triplet state
The presence of an electric field can drift thermalized electrons, preventing them from recombining and reducing the scintillation yield

## Slide 7
Analog Integr Circ Sig Process 111, 387–402 (2022)
Particle Identification by Scintillation pulse shape

## Slide 8
Attenuation Length:
pure Argon is transparent to its own scintillation light
contaminants like Oxygen, Carbon etc., can absorb the scintillation light, leading to a finite attenuation length
Birk’s constant:
Birk’s law is an empirical formula for the light yield of a particle traversing a scintillator:
Background Optical properties of LAr detectors
Birk’s coefficient

## Slide 9
Background Optical properties of LAr detectors
Photomultiplier Tubes (PMTs)
Working mechanism:
An incident photon hits the cathode and emits an electron via Photoelectric effect
A series of dynodes at increasing voltages cause cascade of secondary electrons
A voltage signal is measured in the anode
Photoelectron = signal measured from one photon absorbed by the PMT
In LAr experiments a Wavelength Shifter(WLS) is used to shift scintillation to visible spectrum
Source
Notes: Explain how PMTs work, and about photoelectrons. Also mention typical PMTs not sensitive to Ar scintillation wavelength so need TPB wavelength shifter

## Slide 10: Background Neutron-Ar Interactions
In the relevant energy regime, there are 2 types of interactions:
Elastic: causing a recoil Ar nucleus
Inelastic: neutron interaction with nucleons
Eur. Phys. J. C 84, 1052 (2024)

## Slide 11
Simple transfer of energy
Using kinematics, it is possible to calculate nucleus recoil energy from neutron scattering angle
Background Elastic Scattering in LAr

## Slide 12
(n,n′): neutron creates Ar-41 excited state
De-excites via γ-ray emission and neutron isotropic scattering
Background Inelastic Scattering in LAr

## Slide 13
Dark Matter experiment aiming to measure relative scintillation efficiency of low energy nuclear recoil to that of electronic recoils:
  Where:
  is the nuclear/electronic recoil energy deposit
  is the light yield from a nuclear recoil
  is the light yield from an electronic recoil
Geant4 Simulation Validation Energy deposit calibration
Creus experiment overview

## Slide 14
LAr cell with 2 PMTs and a wavelength shifter.
Neutron source: 2.45 MeV dd-fusion, collimated beam.
Liquid scintillator used to tag scattered neutron.
Geant4 Simulation Validation Energy deposit calibration
Creus Experiment Setup
W. Creus et al 2015 JINST 10 P08002

## Slide 15
Geant4 Simulation Validation Energy deposit calibration
Geant4 setup
Neutron Beam
Liquid Scintillator - Neutron detector
LAr Cells
Notes: Only the main components simulated

## Slide 16
Convert energy deposits → photoelectrons via χ² fit of and resolution R to Creus data
Statistical smearing via Poisson and Gaussian convolution
Geant4 Simulation Validation Energy deposit calibration
Extracting
W. Creus et al 2015 JINST 10 P08002
Geant4 simulation – A.B.P

## Slide 17
Extracted vs recoil energy agrees well with published Creus data
Validates energy deposition
Geant4 Simulation Validation Energy deposit calibration
Simulation comparison with data

## Slide 18
After validating our simulation in terms of energy deposit, we need to validate it in terms of optical photons produced
We use DarkSide and ARIS γ-ray scintillation data to tune optical parameters
Geant4 Simulation Validation Optical Photon Calibration

## Slide 19
Three sources: Na (511,1274 keV), Co (122 keV), Cs (662 keV)
High purity (~30 m attenuation length)
Photopeak positions in good agreement
Geant4 Simulation Validation Optical Photon Calibration
DarkSide Comparison

## Slide 20
Three sources: Na (511,1274 keV), Co (122 keV), Cs (662 keV)
High purity (~30 m attenuation length)
good simulation agreement
Geant4 Simulation Validation Optical Photon Calibration
DarkSide Comparison

## Slide 21
Less pure LAr → attenuation length must be fitted
Calibration performed with Am and Na sources
Geant4 Simulation Validation Optical Photon Calibration
ARIS Comparison

## Slide 22: Challenges Of Simulating Neutron-Induced Scintillation A model problem
Birk’s model too limited:
Same parameters for all particles
Can’t accurately describe different particles’ scintillation at the same time
A more realistic model: Hong model
Separates electronic & nuclear de-excitation behaviour
Data on LAr is lacking for full parameterization

## Slide 23: Correction Strategy
Use Birk’s model with a correction given by empirical values of
PHYS REV D 97, 112005 (2018)

## Slide 24: Correction Strategy The correction
Fit optical parameters based on data, per experiment/detector
Notes: In each event i, we use GEANT4 to simulate a neutron impinged on LAr with energy , depositing in the desired reaction, and producing scintillation photons. These scintillation photons propagate to the optical sensors and produce photoelectrons.
• Since we do not trust , we make the correction , where is the number of scintillation photons that should have been produced at event i based on ΔEᵢ — based on empirical data.
In each event i, we use GEANT4 to simulate a neutron impinged on LAr with energy 𝐸_𝑛, depositing Δ𝐸_𝑖 in the desired reaction, and producing 𝑁_𝑝ℎ scintillation photons. These scintillation photons propagate to the optical sensors and produce 𝑁_𝑝𝑒 photoelectrons.
• Since we do not trust 𝑁_𝑝ℎ, we make the correction 𝑁_𝑝𝑒→𝑁_𝑝𝑒^∗=𝑁_𝑝𝑒×(𝑁_𝑝ℎ^∗)/𝑁_𝑝ℎ , where 𝑁_𝑝ℎ^∗ is the number of scintillation photons that should have been produced at event i based on ΔEᵢ — based on empirical data.

## Slide 25: Correction Strategy The correction
On event-by-event basis, make the correction:
Number of photons produced
Number of photons which should have been produced
Number of photoelectron measured
Fit parameters
Notes: In each event i, we use GEANT4 to simulate a neutron impinged on LAr with energy , depositing in the desired reaction, and producing scintillation photons. These scintillation photons propagate to the optical sensors and produce photoelectrons.
• Since we do not trust , we make the correction , where is the number of scintillation photons that should have been produced at event i based on ΔEᵢ — based on empirical data.
In each event i, we use GEANT4 to simulate a neutron impinged on LAr with energy 𝐸_𝑛, depositing Δ𝐸_𝑖 in the desired reaction, and producing 𝑁_𝑝ℎ scintillation photons. These scintillation photons propagate to the optical sensors and produce 𝑁_𝑝𝑒 photoelectrons.
• Since we do not trust 𝑁_𝑝ℎ, we make the correction 𝑁_𝑝𝑒→𝑁_𝑝𝑒^∗=𝑁_𝑝𝑒×(𝑁_𝑝ℎ^∗)/𝑁_𝑝ℎ , where 𝑁_𝑝ℎ^∗ is the number of scintillation photons that should have been produced at event i based on ΔEᵢ — based on empirical data.

## Slide 26: Summary
interactions produce scintillation light
simulating – induced scintillation can improve energy reconstruction by assisting neutron detection in LArTPCs
Validated Geant4 simulation in terms of energy deposit and optical photon production

## Slide 27: Future goals

## Slide 28: Future goals
Build comprehensive simulation for TAU Lab
Calibrate LAr test-stand with sources, then measure low energy neutron scintillation (using dd-generator)
Final goal: simulate/measure high-E neutron scintillation response.

## Slide 29: Background Interaction type breakdown
Distribution of interaction types at 10 MeV shows dominance of elastic + (n,n').
Important for modeling expected light yields and neutron ID.

## Slide 30
Simple transfer of energy; calculable from neutron scattering angle.
Elastic scatter kinematics are given by
where is the recoil nucleus’ kinetic energy, A is the atomic number (40 for Ar), is the neutron’s initial kinetic energy and is the neutron scattering angle
Background Elastic Scattering in LAr
Make sure to understand how to derive this

## Slide 31
Creus et al. used Geant4 based monte carlo to analyze their results
Only track and energy deposits were simulated – no scintillation photons
Event selection
Several cuts are used to maximize single elastic events while minimizing background
Time of flight – using signals from LAr cell and the liquid scintillator
which distinguishes accidental x-rays and γ rays by looking at theratio of the prompt light to the later light
Geant4 Simulation Validation Energy deposit calibration
Creus Experiment Setup

## Slide 32
From energy deposit to photoelectrons
Since they did not simulate scintillation, a response function is needed to obtain number of photoelectrons (p.e.) from energy deposit:
Geant4 Simulation Validation Energy deposit calibration
Extracting
Resolution smearing
Resolution of 1pe PMT signal
Measured Light Yield
Energy deposit

## Slide 33
Geant4 Simulation Validation Energy deposit calibration
Extracting
The best fit parameters R, are determined via a fit by comparing the calculated spectrum of p.e. in simulation to the data:

## Slide 34
Geant4 Simulation Validation Optical Photon Calibration
DarkSide Comparison

## Slide 35
Geant4 Simulation Validation Optical Photon Calibration
DarkSide Comparison

## Slide 36
Geant4 Simulation Validation Optical Photon Calibration
ARIS Comparison